## Slide 1: Ion impact distributions of DS collimators in IP2
Michaela Schaumann
02/05/2013

## Slide 2: Motivation
Installation of collimators in the Dispersion Suppressor (DS) to both sides of ALICE (IP2) to intercept secondary beams from bound-free pair production (BFPP) and electromagnetic dissociation (EMD) .
Main: 208-Pb-82+
BFPP1: 208-Pb-81+
BFPP2: 208-Pb-80+
EMD1: 207-Pb-82+
EMD2: 206-Pb-82+
The rigidity of each
beam changed by

## Slide 3: General Procedure
Editing the sequence and add DS collimator in IP2.
Calculating the transfer matrix form IP to front of collimator with MADX.
Convert MADX output into desired format for FLUKA.
Generation of the
distribution at the IP.
Tracking of distribution
to front of collimator.
Calculate σ-Matrix
at IP.
Tracking of σ-Matrix
to front of collimator.

## Slide 4: Editing the sequence
Modified Sequence
Nominal Beam Line
IP2
Magnet to be replaced MB.A10R2
2 11T dipole with L = 5.3m
Collimator jaw with L = 1m

## Slide 5: Editing the sequence – Influence on Optics
Orbit change in X and Y
Dispersion change in X and Y
β-Beat in X and Y
Without taking magnet errors into account the changes in the optics are very small.

## Slide 6: Editing the sequence – Influence on Optics
MADX Survey
Coordinate System

## Slide 7: Transfer Matrix
Do TWISS with initial conditions at the IP and RMATRIX flag on:
→p= x, y, px/(1+), py/(1+)
with x, y, px, py of the main beam orbit at IP2.
This generates TWISS table with transfer matrix elements after each element in the sequence.
MADX 6D Transfer Matrix:
→ form IP2 @ s = 0m
→ to new front plane of collimator @ s = 356.27m

## Slide 8: Tracking
where x = (x, px, y, py, t, pt)
and M = (6 6 ) transfer matrix
A.)
B.)
Generate coordinates for each particle at IP and track them with transfer matrix M:
Calculate σ-Matrix at IP and track envelope:
where M = (6 6 ) transfer matrix
and

## Slide 9: A.) Generating distribution @ IP
R. Bruce et al., Beam losses from ultraperipheral nuclear collisions between 208Pb82+ ions in the Large Hadron Collider and their alleviation, Phys. Rev. ST Accel. Beams 12, 071002 (2009)
Assume Gaussian Distribution of the main beam:
Distribution of collision point at the IP:
→ Gaussian distribution with smaller standard deviation .
→ The standard deviation of the angular distribution is similar to the main beam.
Generate

## Slide 10: A.) Generating distribution @ IP
Generate
The longitudinal positions of the particles are not important for this analysis, since the impact point (front plane of the collimator) is fixed for this first attempt:
→ set them all to t = 0 at the IP.
Assume that the pt values are Gaussian distributed around <pt>=0 at the IP,
→ take the change in rigidity into account when generating the transfer
matrix for a beam with a given .

## Slide 11: A.) Generating distribution @ IP
Example
coordinates
of 1000
particles at
the IP
x
x’
y
y’
t
δpt

## Slide 12: B.) Calculate σ-Matrix @ IP
Distribution of collision point at the IP:
σ-Matrix @ IP:
and
where

## Slide 13: Tracking Results
Example
coordinates
of 1000
particles at
the collimator:
A.)Coordinate
B.) σ-Matrix
Tracking
Coordinates for B.)
Generate Gaussian distributions with
mean = orbit coordinates,
std. dev.= σ-matrix diagonal elements.
x
x’
y
y’
δpt

## Slide 14: Tracking Results
Coordinates of the orbit for a beam with p = BFPP at the collimator:
Mean of tracked Coordinates :
Standard Deviation of tracked Coordinates :
Diagonal Elements of σ-matrix at the collimator :

## Slide 15: Conversion to FLUKA input
Positions and angles on collimator:
- x, x’, y, y’ taken as calculated above in units of .
- t = s = 356.27m (collimator front plane) for all particles.
pt → Energy E
with

## Slide 16: Simulation Scenarios
How much of the other beams is absorbed if ασ of the BFPP1 beam are intercepted by the collimator jaw?
What effect does the length of the collimator have on the absorption of the produced shower?
What beam properties should be used?
BFPP1
½ - gap
central orbit
β = 151m (at collimator front)
= 3.5μm/ γ
γ = 6.5TeV/0.938GeV

## Slide 17: Things to be done…
Discuss how to proceed with FLUKA runs: Initial model of simple jaw
Intercept other secondary beams from IP (EMD1, BFPP2, EMD2, …) as function of collimator gap (reduce losses in IR3 and elsewhere).
Other positions of the collimator?
Check influence of change in sequence on optics → include magnet errors?
Other optics cases
Calculations for B2 on left side of IP2.