## Slide 1: Updated Design of TCLD whit reduced jaw length Collimation Upgrade Specification meeting 18-10-2013 L. GENTINI

## Slide 2
Contents
  Overview
  Preliminary design study
    Actuation system
    Vacuum tank
    Jaws
    Cooling system
    Instrumentation
  Status

## Slide 3
Overview
QTC
TCLD
Unchanged length
Unchanged length
New collimator length 1280 mm
100 mm
100 mm
Manual quick connecting flange: unavailable remote handling
Sector valves
Ion pumps
Current QTC

## Slide 4
Collimator assembly
Actuation system
“V” interconnection points. Collimator replacement without realignment
Collimator
Support assembly
Alignment assembly
  The support assembly will be the same of the TCDQ

## Slide 5
Actuation system
To be changed
Recovered
  Frame
  Partially recovered from existing TCLD actuation system
  Movement
  No jaw tilting
  Stroke: 0  25 mm
  One step motor each jaw
  Spring-back: in case of electrical short-cut the jaws must not go in beam direction
  Instrumentation
  3x LVDT (1x each jaw, 1x anti-collision)
  3x switch assemblies (1x each jaw, 1x anti-collision)
  Alignment
  Adjusting assembly with 2x laser trackers
To be changed
To be changed
To be changed
Recovered
Recovered
  Jaw actuation

## Slide 6
jaws
BPM cables
Extremity RF contacts
  General
  Active length reduced by 200 mm (1000  800 mm)
  Brazed jaws
  4x screwed tungsten blocs each jaw
  Tapering slopes 10°and 15°
  Cantilever jaws
  Cooling system
  Square pipes (9 mm edge, CuNi)
  3x cooling pipes in the central cross-section
  Instrumentation
  2x temperature probes (TP100) each jaw
  2x Beam Position Monitor each jaw
  BPM cables: same electrical length of TCTP with different shape
  RF system
  Ferrite tiles + St. steel screens
  Vacuum tank based on Ph.II collimator
BPM
800 mm
1000 mm
Old design
New design

## Slide 7
Jaw details
Tungsten blocs
Ferrite tiles
Ferrite tiles
RF screens St. Steel
RF screens St. Steel
Bloc Support Glidcop
Back stiffener Glidcop
Tank axis
Cooling pipes CuNi
40

## Slide 8
Jaw details
BPM
Tapering slope : 10°
RF screen St. Steel
Tapering slope : 15°
Screen RF contact CuBe C17410
Extremity RF contact CuBe C17410
RF contact CuBe C17410
Screen RF contact CuBe C17410

## Slide 9
Jaw details
Ferrite tiles
Tungsten blocs
Ferrite tiles

## Slide 10
Tcld updated design status
18-10-2013 | Study | 3D models | Drawings | Controls | Manufacturing
Actuation System | 100% | 95% | 70% | 70% | 60%
Jaws | 80% | 70% | 30% | 0% | 0%
Tank | 100% | 100% | 50% | 0% | 0%
Support | 100% | 100% | 0% | 0% | 0%
Jacks | 70% | 70% | 70% | 70% | 70%
Test tools | 30% | 30% | 20% | 20% | 20%

## Slide 11
  Thank you for your attention!