## Slide 1
STATUS of BBC DESIGN and ENGINEERING : PRELIMINARY RESULTS G. MAITREJEAN, L. GENTINI

## Slide 2: Outline
Specifications:
Re-use nearly 100% of existing TCTP design
Electrified wire as close as possible to the beam axis:
  distance the center of the wire - the surface of the jaw <3mm
Maximum diameter of the copper 2mm
Maximum input current: 350A DC
If possible, 2 wires (1 working – 1 spare)
Beam-Beam compensator:
Decreasing the influence of a beam on the other using electrified wire in some TCTP collimators

## Slide 3: 1 Wire Design
Cooling Pipes (Cu Ni)
Tungsten Jaw (Inermet)
Glidcop Jaw (Glidcop)
Back-Stiffener (Glidcop)
3mm
17mm

## Slide 4: 2 Wires Design
Cooling Pipes (Cu Ni)
Tungsten Jaw (Inermet)
Glidcop Jaw (Glidcop)
Back-Stiffener (Glidcop)
3mm
11.4mm

## Slide 5: 1 Wire Design

## Slide 6: 2 Wires Design

## Slide 7: Wire
Thermocoax wire
3 Layers
Total diameter : 3.6mm
Electrical properties :
Magnesium Oxide layer perfect electrical insulator
Copper very good electrical conductor
Maximum admissible temperature (estimated by Thermocoax, not tested): ≈400ºC
(under testing by A. Ravni)
Stainless Steel – Thickness 0.3mm
Magnesium oxide – Thickness 0.5mm
Copper – Diameter 2mm

## Slide 8: TCTP Thermal Load
TCTP without BBC
  1h Beam Life Time (8.6e8 p/s) on each Jaw : 418.4W
TCTP with BBC
Heat generation due to Joule effect in the wire with 350 A :
2.11e8 W/m³ (at 300ºK)
Total thermal power dissipation:
  1 Wire design at 300ºK : 940 W + 418W from beam
  2 Wires design at 300ºK : 986 W + 418W from beam
  BBC : adds more than twice the 1h BLT thermal load
  optimisticaly assuming RT Cu electric resistivity

## Slide 9: Thermal simulation : wire cooled only in Jaw
Calculation for both designs: 1 and 2 wires
Only electric load considered: 350A DC current
To achieve numerical convergence, electric load applied through internal heat generation
Power calculated from Joule heating 350A DC at 27ºC = 2.11e8 W/m³
9000 W/(m²K)
18000 W/(m²K)
2100 W/(m²K)
6500 W/(m²K)
Thermal interfaces
Heat sink : convection inside cooling pipes
13000 W/(m²K)

## Slide 10: 1 Wire
Temperature max
Inermet Jaw: 101.1ºC
Wire: 15800ºC
Average temperature
Inermet Jaw : 34ºC
Glidcop Jaw : 31.4ºC

## Slide 11: 2 Wires
Temperature max
Jaw: 116.8ºC
Wire: 19600ºC
Average temperature
Inermet Jaw : 36.6ºC
Glidcop Jaw : 31ºC

## Slide 12: Additional thermal bridge system
Glidcop
Stainless Steel

## Slide 13: 1 Wire – Optimized Cooling system
Temperature max
Tungsten Jaw: 42.1ºC
Wire: 440ºC
Average temperature
Inermet Jaw : 32.5ºC
Glidcop Jaw : 30ºC

## Slide 14: 2 Wires - Optimized Cooling system
Temperature max
Tungsten Jaw: 49.2ºC
Wire: 431ºC
Average temperature
Inermet Jaw : 34.6ºC
Glidcop Jaw : 29.7ºC
350A DC not compatible with present design

## Slide 15: Thermal issues
Electric resistivity not constant over temperature : the hotter, the higher the heat generation
Chart: Copper
| -73 | 27 | 127 | 227 | 327 | 427 | 527 | 627 | 727 | 827 | 927 | 1027
 | 1.044e-08 | 1.72e-08 | 2.4e-08 | 3.09e-08 | 3.79e-08 | 4.51e-08 | 5.26e-08 | 6.04e-08 | 6.86e-08 | 7.72e-08 | 8.62e-08 | 9.59e-08
Electric resistivity at 400ºC = 2.5 times the one at 27ºC
Temperatures reached are clearly underestimated

## Slide 16: Preliminary conclusion : Thermal issues
Both designs not acceptable (yet !)
Challenge: must cool the wires in the hottest zones!
50mm
20ºC
20ºC
350 A
350 A DC with constant electric resistivity at RT
350 A DC with T-dependant electric resistivity
Taking into account dependency in T :
Strong increase of the final temperature

## Slide 17: Back-up slide

## Slide 18: Back-up slide
2 Wires design - Thermal load: 350 A with constant electric resistivity (at 400ºC)

## Slide 19: Back-up slide
2 Wires design - Thermal load: 300 A with constant electric resistivity (at 27ºC)