## Slide 1: Preliminary integration of Hollow e-lenses EDMS No: 1764989 v.2 (V.1. Presented on 26th TCC 16/03/2017) References: 1765930.v.1
M. Alcaide Leon, Paolo Fessia
Contributions
HEL conceptual design and parameters: D. Perini, C. Zanoni Beam optics and HEL technical coordination: A.Rossi
HEL 3D Modelling: A. Kolehmainen
3D Integration Modelling: M. Gonzalez QPS requirements: D. Wollmann, R. Denz, A. Verweij
Power Converters requirements: M. Martino & Y. Thurel Vacuum requirements: P. Santos
Cryogenics requirements: S. Claudet
EDMS No: 1764989 v.2. 22/05/2017
Draft

## Slide 2: INDEX
    Preliminary integration of HEL in HL-LHC machine and technical services in the tunnel of 4L
    Preliminary integration of technical services in service caverns of 4L
    Conclusions

## Slide 3: REMARK
    This is a preliminary integration study of the Hollow e-lenses in the machine lay-out for HL-LHC and its technical services in the tunnel and service caverns with the present conceptual design of the device (EDMS No: 1765930.v1). The conceptual design is subject to change due to further technical optimizations and definitions by the WPs involved in its design. In particular possible integration in the Hollow e-lenses of Beam Instrumentation that are not accounted here and for which the possible impact on the device and layout is not known.

## Slide 4
Preliminary integration of HEL in HL-LHC machine and technical services in the tunnel of 4L*
*Please note that 4R is symmetric to 4L

## Slide 5: Overview of LSS4 P4L
UA43
RA43
UJ44
UL44
US45
RB44
B2
D3L4
HEL
ADT
ACS
B1
ST0676534_01

## Slide 6
HEL – Dimensions
Previous design was used in May 2017.
Integration being redone with new optimized design

## Slide 7
HEL – Dimensions
New optimized design
Previous total length used for this integration 6171 mm
New design total length used for this integration 6630 mm

## Slide 8: Layout integration in HL-LHC machine
ST0676534_01
D3
DFB
HEL
V.C Supports
Ventilation door
ADT
ST0676534_01
Images to be updated

## Slide 9: Interface with other equipment in the tunnel
  Cryogenics supply:
    New dedicated service module and jumper. Options:
      Possibility to install one dedicated service module for HEL leaving space for a future service module for new xxxMHz module or,
      install a double service module with two jumpers for HEL and future xxxMHz module
ST0676534_01

## Slide 10: Tunnel general services
  Water cooling pick up for collector: needed. Integration being studied
  Services for e-gun powering:
    1 or 2 modulators placed under the e-lens.
Available space under HEL:
- Width: 2 m (space between jacks)
- Depth: 1m
- Height: 500mm
Modulator envelope
- 50x50 cm x 30cm height

## Slide 11
Preliminary integration of technical services in Service caverns of 4L*
*Please note that 4R is symmetric to 4L

## Slide 12: Power supplies - Circuit rating
450 A
450 A
  Total number of independent circuits: 17
      7 PC x HL-LHC600A-10V
      10 PC x Cancun 50
  Total number of racks: 6 PC racks + 1 control rack
    Spare slots taken into account
    Water cooling for HL-LHC600A-10V

## Slide 13: Power supplies - Characteristics
  Cabling characteristics:
    Waiting for AC and DC cabling definition and integration
    First check from EN-EL Installed power in UA43/47 should be enough

## Slide 14: HEL – Other racks needs
  QPS:
    EE system needed? Study by WP7 to see if they are self protected
    Racks  2 min, 6 max (if EE needed)
    Location: together with the PCs
  BI: 2 racks for control
  E-gun:
    An Electrical Cabinet roughly, 2m wide, 1.2m deep, and 2.5m high. Into this cabinet all equipment at 15kV potential. (water cooling no needed)
    A standard 19 inches rack with control electronics, cathode PC (referred to ground) and the main circuit breaker
    Integration of these 2 elements is being studied
To be revised

## Slide 15: Racks needs summary
System | Min. racks | Max. racks
Power converters | 7 | 8
QPS | 2 | 6
BI | 2 | 2
E-gun | 1 | 2
Total | 12 | 18

## Slide 16: Option 1: UA43 & UL44 (P4L) / UA47 & UL46 (P4R)
UA43
14 racks
4 racks
Racks- Location
UL44

## Slide 17: Option 2: UA43 (P4L) / UA47 (P4R)
Racks- Location
4 racks or more
UA43
14 racks
4 racks or more

## Slide 18
Conclusions

## Slide 19: Overview of LSS4 P4L until D4 for HL-LHC
BSR - New extraction and hutch
BSR - Old extraction and hutch
NEW ADT: existing reservation
B2
B1
HEL and racks
UA43
ST0676534_01

## Slide 20: HEL – Conclusions
  In view of a possible technological and integration review in autumn this year the integration and service analysis should be updated taking into account:
    Results of EE computation
    Addition of Beam Instrumentation equipment and its impact on the HEL design and of the general services requirements
    A detailed analysis of other ancillary equipment that should be placed in the LHC tunnel (e-gun ancillaries?)
    Cabling routing from PC to HEL should be defined and integrated

## Slide 21
Thank you

## Slide 23
Extra slides

## Slide 24: HEL- Optics
Courtesy of Adriana Rossi

## Slide 25: Layout integration in HL-LHC machine
ST0574939_01
New design of vacuum chamber supports to gain some space

## Slide 26: Sketch layout with HEL - 4L
Total length of RF zone (from HEL to IP): 37357 mm
Distance from IP4: 43529 mm

## Slide 27: Interface of HEL with other equipment
    Vacuum pressure during operation must be lower 10-11 mbar.
    Vacuum chamber NEG coated.
    Vacuum chamber inner diameter: 80 mm.
    Vacuum chamber material: cooper.
    Bake-out temperature: 250°C.
    25 mm bake-out jacket.
    Sector valve for the e-gun:
      Exchange procedure to be study.
    The design of the collector should avoid degassing.
      In case of collector degassing, ion pumps or in worst case 1 m length NEG coated vacuum pipe on both sides of the HEL should be installed. (Not in present layout proposal) → to be studied by the HEL team and WP12.
    2 x Current Transformer
    2 x Beam Position Monitor
    2 x Gas Jet Monitor
135mm
Vacuum:
BI:
454 mm

## Slide 28: Interface of HEL with other equipment
135mm
BI:
454 mm
From inside to outside in grey the room temperature vacuum tank, in brown the thermal screen, in grey the helium tank wall, in orange the main solenoid, in blue the corrector coils generating a horizontal and a vertical dipole. Then follow the helium tank wall, the thermal screen and the vacuum tank. The overall external diameter is 454 mm.

## Slide 29: Sketch layout in case of possible RF upgrade

## Slide 30: Sketch layout in case of possible RF upgrade with arbitrarily longer HEL (+500 mm for instrumentation)

## Slide 31: HEL – Conclusions
System | Type | Description | Actions
Gas Position Monitor | Open option | It will increase the length of the device, therefore decrease space between HEL and BPM after ADT | Wait to see if it is going to be included
Gun and collector degassing | Design optimization | Design of electrons gun and collector to avoid degassing, otherwise 1m of vacuum chamber in both extremes of HEL with NEG coating needed | Design of the collector avoiding degassing
Space for pumps | Design optimization | Not so much space for the ion pump in e-gun | Interaction with Vacuum for HEL design
Supports for vacuum chamber | Design optimization | Support of vacuum chamber between HEL and Valve takes space maybe needed | Design of new supports
Racks options | Integration study | Two options for racks, depending on total number of racks needed and space availability | Conduct integration studies
Cryogenic supply | Technical study | Two options for cryogenic supply | Conduct studies
EE | Technical study | On-going study to see if the coils are self-protected, it will save space for EE racks | Wait for results
DC Cabling | Study | DC cabling and integration has to be studied | Conduct studies