## Slide 1: E-GUN Hollow Electron Lens
HEL E-GUN Design Review
30/1/2020
antti.juhani.kolehmainen@cern.ch

## Slide 2: OVERVIEW
MOTIVATION
OVERVIEW
FUNCTIONAL GEOMETRY
ELECTRICAL CONNECTIONS
GAPS BETWEEN COMPONENTS
HEAT LOADS AND CERAMICS
MECHANICAL TOLERANCES
DESIGN OFFICE TO DO
CONCLUSION

## Slide 3: MOTIVATION
TO SOLVE ISSUES OF THE FIRST CERN DESIGNED E-GUN FOR THE HEL
TO CREATE DESIGN FULLY COMPATIBLE WITH THE HEL

## Slide 4: INSPIRATION – TEL E-Gun Design
LHCNECGP0075
CHG-16-sc
LHCNEHE_0026
DESIGNED FOR THE HOLLOW ELECTRON LENS!

## Slide 5: MAIN DIMENSIONS
MASS ≈ 10 kg

## Slide 6: FIT TO THE FERMILAB TEST STAND
ADJUSTMENT CHAMBER POSITIONS GUN CORRECTLY
INTEGRATION TO THE TEST STAND TO BE VERIFIED BY THE FERMILAB TEAM
  Total length increased
  Access to the flange connection
  3D available from CERN

## Slide 7: FUNCTIONAL GEOMETRY
LHCNECGP0075
CHG-16-sc
LHCNEHE_0026
LHCNEHEP0001 – CHG-16-sc-e)
LHCNEHEP0014
CORRECT WHEN SCALED FROM 25.4 mm E-Gun!

## Slide 8: ELECTRICAL CONNECTIONS
CATHODE WIRES IN Ø1 mm NICKEL
GUIDED WITH REGULAR CERAMIC PIECES IN MACOR
CONTROL ELECTRODE IN Ø1.27 mm COPPER
CONNECTED TO THE BASE FLANGE

## Slide 9: ELECTRICAL CONNECTIONS
ANODE SUPPORT ELECTRICALLY FLOATING!
CERAMIC STAND-OFF TO ISOLATE
ANODE FROM SUPPORT
ANODE WIRE GUIDED THROUGH
SHORT CERAMIC TUBES CONNECTED TO THE ANODE SUPPORT

## Slide 10: CATHODE – CONTROL ELECTRODE GAP
POTENTIAL DIFFERENCE < 1000V
GAP IN VACUUM ~ 2 mm
GAP THROUGH CERAMIC ~ 14 mm

## Slide 11: CATHODE – GROUND GAP
POTENTIAL DIFFERENCE ≤ 15 kV
GAP IN VACUUM ~ 4.5 mm
GAP THROUGH CERAMIC ~ 19 mm

## Slide 12: CATHODE – ANODE GAP
POTENTIAL DIFFERENCE ≤ 15 kV
GAP IN VACUUM ≈ 5.3 mm
GAP THROUGH CERAMIC = GAP TO GROUND:
1. CATHODE TO GROUND ≈ 19 mm
2. ANODE TO GROUND ≈ 21 + 15 mm

## Slide 13: CONTROL ELECTRODE – ANODE GAP
POTENTIAL DIFFERENCE ≤ 15 kV
GAP IN VACUUM ≈ 5.5 mm
GAP THROUGH CERAMIC ≈ 21 + 15 mm

## Slide 14: MECHANICAL TOLERANCES
ALLOWED ERROR?
  CATHODE – ANODE
  CATHODE – CONTROL ELECTRODE
ACHIEVABLE TOLERANCES BEING DISCUSSED WITH CERN EN/MME WORKSHOP
ADJUSTABILITY:
  CATHODE – ANODE SPACING WITH RE-MACHINABLE SHIM = EASY
  CATHODE – ANODE ALIGNMENT WITH RE-MACHINABLE SHIM = RELATIVELY EASY
  CATHODE – CONTROL ELECTRODE LONGITUDINAL SPACING WITH CONTROL ELECTRODE REMACHINING
  CATHODE – CONTROL ELECTRODE ALIGNMENT WITH CONTROL ELECTRODE REMACHINING OR FORMING = NOT EASY
COMPONENT DEFORMATION UNDER OPERATION TO BE STUDIED
BEST POSSIBLE ESTIMATION FOR COMPONENT TEMPERATURES REQUIRED

## Slide 15: HEAT LOAD
Courtesy of Sergey Sadovich

## Slide 16: CERAMICS AROUND THE CATHODE
20 mm
43 mm
11 mm

## Slide 17: CERAMICS AT DISTANCE
217 mm
WIRE SUPPORTS AT 100, 150 and 215 mm FROM THE CATHODE

## Slide 18: TACKLING THE HEAT – AND LEAK CURRENT
RADIATORS
COPPER SUPPORT FOR HEAT CONDUCTION
HEAT SHIELD
CUT-OUTS TO REDUCE SURFACE AREA FOR HEAT CONDUCTION

## Slide 19: DESIGN TASKS TO DO
MACHINED SPRING TO CLAMP COMPONENTS:
MUST ALLOW TOLERANCES
MUST ALLOW THERMAL EXPANSION
ANODE POSITION w.r.t. CATHODE
PRECISION ↑ COMPLEXITY ↑
INDICATION REQUIRED

## Slide 20: DESIGN TASKS TO DO
DEFORMATION OF
CATHODE SUPPORT
CONTROL ELECTRODE
ANODE SUPPORT
FINISH MANUFACTURING DRAWINGS, ≈ 75 % CREATED
YOUR FEEDBACK TO IMPLEMENT!

## Slide 21: OPTIONAL CONCEPT
SHORTER CATHODE SUPPORT AND CONTROL ELECTRODE → SMALLER TOLERANCE LEVER-ARM
MORE COMPLEX CERAMIC SUPPORT
SIMILAR ANODE ALIGNMENT SCHEME WITH RE-MACHINABLE SHIM

## Slide 22: CONCLUSION
TWO CONCEPTS CREATED TO TACKLE THE LEAK CURRENT ISSUE AND TO FIT TO THE HEL – FIRST ONE BEING DETAILED
ALIGNMENT OF FUNCITONAL GEOMETRY TO BE CONFIRMED
THERMAL ANALYSIS DESIRED
MANUFACTURING OF THE FIRST VERSION PREVIEWED – NO SHOWSTOPPERS

## Slide 23
THANK YOU FOR YOUR ATTENTION!
!/?
YOUR QUESTIONS PLEASE!