## Slide 1: Optics flexibility in IR3/7
Massimo Giovannozzi
  Acknowledgements: P. Fessia, S. Redaelli, T. Risselada.
Remark: design effort to analyse possible improvements to the IR optics on-going (S. Fartoukh).

## Slide 2: Injection configurations - I
New optics in IR3/7?
  Trigger: recuperate warm magnets to increase the number of spares. Preliminary conclusions:
    In IR3 no MQWB can be removed without changing the optical conditions at the collimators.
    In IR7 the MQWB modules in the two Q5 may be removed without changing the optical conditions at the collimators (2 spare magnets).
    Any other change in the layout will generate a difference of optical condition at the location of the collimators -> Detailed validation of the optics with simulations is required before taking any decision.
  Option to be explored in more details!
Analysis made by T. Risselada

## Slide 3: Injection configurations - II
Alternative approach (after input from P. Fessia):
  Highest dose delivered to the first magnet making the Q5 in IR7.
  It could be advantageous to replace it with an absorber :
    Detailed evaluation of the dose reduction to the second magnet by the installation of an absorber still to be done.
    Time horizon of this change: LS2
  Therefore:
    Instead of removing the MQWB it should be re-configured as an MQWA.
    This would restore the total integrated strength after replacement of one MQWA with an absorber.
    All this corresponds to displacing the Q5 longitudinally:
      Can the optics be kept reasonably constant in the collimation region?